Pressure tank:
For tank pressure, we will simply use a bike pump with a valve on the pressure tank. The pressure tank will be leak tested underwater (to see bubbles to locate leak) and will be put in an over-pressure state in order to test its ability to withstand high pressures.
The tank could be pressurized first, with no water, then fill the tank with water from the launch clamp (Gardena threaded hose connector (Article No. 917-50)) in order to easily increase the pressure of the compressed air.
Maybe, the tank could be reinforced with Duct Tape.

Nozzle:
Could be a Gardena Tap Connector (G3/4”) (Article No. 18201-20)

Launchpad:
A Gardena threaded hose connector (Article No. 917-50) could be used, as it has a simple release mechanism with proper sealing methods. A powerful servo or solenoid could then pull down on the connector to trigger the release of the rocket.

Refs:
Gardena threaded hose connector (Article No. 917-50): https://www.gardena.com/int/products/watering/hose-fittings/threaded-hose-connector-26-5-mm-g-3-4/900874401/

Gardena Tap Connector (G3/4”) (Article No. 18201-20): https://www.gardena.com/int/products/watering/hose-fittings/tap-connector-26-5-mm-g-3-4/967312101/